## Slide 1: CS162 Operating Systems and Systems Programming Lecture 15 Memory 3: Caching and TLBs (Con’t), Demand Paging
March 11th, 2021
Profs. Natacha Crooks and Anthony D. Joseph
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: The two-level page table
Physical
Address:
Offset
Physical
Page #
4KB
10 bits
10 bits
12 bits
Virtual
Address:
Offset
Virtual
P2 index
Virtual
P1 index
4 bytes
PageTablePtr
Tree of Page Tables
  “Magic” 10b-10b-12b pattern!
Tables fixed size (1024 entries)
  On context-switch: save single PageTablePtr register (i.e. CR3)
Valid bits on Page Table Entries
  Don’t need every 2nd-level table
  Even when exist, 2nd-level tables can reside on disk if not in use
4 bytes

## Slide 3: Recall: Caching Applied to Address Translation
Question is one of page locality: does it exist?
  Instruction accesses spend a lot of time on the same page (since accesses sequential)
  Stack accesses have definite locality of reference
  Data accesses have less page locality, but still some…
Can we have a TLB hierarchy?
  Sure: multiple levels at different sizes/speeds
Data Read or Write
(untranslated)
CPU
Physical
Memory
TLB
Translate
(MMU)
No
Virtual
Address
Physical
Address
Yes
Cached?
Save
Result

## Slide 4: Recall: A Summary on Sources of Cache Misses
Compulsory (cold start or process migration, first reference): first access to a block
  “Cold” fact of life: not a whole lot you can do about it
  Note: If you are going to run “billions” of instruction, Compulsory Misses are insignificant
Capacity:
  Cache cannot contain all blocks access by the program
  Solution: increase cache size
Conflict (collision):
  Multiple memory locations mapped to the same cache location
  Solution 1: increase cache size
  Solution 2: increase associativity
Coherence (Invalidation): other process (e.g., I/O) updates memory
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 5: How is a Block found in a Cache?
Block is minimum quantum of caching
  Data select field used to select data within block
  Many caching applications don’t have data select field
Index Used to Lookup Candidates in Cache
  Index identifies the set
Tag used to identify actual copy
  If no candidates match, then declare cache miss
Block
offset
Block Address
Tag
Index
Set Select
Data Select

## Slide 6: Review: Direct Mapped Cache
:
0x50
Valid Bit
:
Cache Tag
Byte 32
0
1
2
3
:
Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 33
Byte 63
:
Byte 992
Byte 1023
:
31
Direct Mapped 2N byte cache:
  The uppermost (32 - N) bits are always the Cache Tag
  The lowest M bits are the Byte Select (Block Size = 2M)
Example: 1 KB Direct Mapped Cache with 32 B Blocks
  Index chooses potential block
  Tag checked to verify block
  Byte select chooses byte within block
Ex: 0x50
Ex: 0x00
Cache Index
0
4
31
Cache Tag
Byte Select
9
Ex: 0x01
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 KB direct mapped cache with block size equals to 32 bytes.
In other words, each block associated with the cache tag will have 32 bytes in it (Row 1).
With Block Size equals to 32 bytes, the 5 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K byte, the upper 32 minus 10 bits, or 22 bits of the address will be stored as cache tag.
The rest of the address bits in the middle, that is bit 5 through 9, will be used as Cache Index to select the proper cache entry.
+2 = 30 min. (Y:10)

## Slide 7: Review: Set Associative Cache
Cache Index
0
4
31
Cache Tag
Byte Select
8
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Mux
0
1
Sel1
Sel0
OR
Hit
N-way set associative: N entries per Cache Index
  N direct mapped caches operates in parallel
Example: Two-way set associative cache
  Cache Index selects a “set” from the cache
  Two tags in the set are compared to input in parallel
  Data is selected based on the tag result
Compare
Compare
Cache Block
Notes: This is called a 2-way set associative cache because there are two cache entries for each cache index. Essentially, you have two direct mapped cache works in parallel.
This is how it works: the cache index selects a set from the cache. The two tags in the set are compared in parallel with the upper bits of the memory address.
If neither tag matches the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data on the side where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 8: Review: Fully Associative Cache
Fully Associative: Every block can hold any line
  Address does not include a cache index
  Compare Cache Tags of all Cache Entries in Parallel
Example: Block Size=32B blocks
  We need N 27-bit comparators
  Still have byte select to choose from within block
:
Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Valid Bit
:
:
Cache Tag
0
4
Cache Tag (27 bits long)
Byte Select
31
=
=
=
=
=
Ex: 0x01
Notes: While the direct mapped cache is on the simple end of the cache design spectrum, the fully associative cache is on the most complex end.
It is the N-way set associative cache carried to the extreme where N in this case is set to the number of cache entries in the cache.
In other words, we don’t even bother to use any address bits as the cache index.
We just store all the upper bits of the address (except Byte select) that is associated with the cache block as the cache tag and have one comparator for every entry.
The address is sent to all entries at once and compared in parallel and only the one that matches are sent to the output. This is called an associative lookup.
Needless to say, it is very hardware intensive. Usually, fully associative cache is limited to 64 or less entries.
Since we are not doing any mapping with the cache index, we will never push any other item out of the cache because multiple memory locations map to the same cache location.
Therefore, by definition, conflict miss is zero for a fully associative cache. This, however, does not mean the overall miss rate will be zero.
Assume we have 64 entries here. The first 64 items we accessed can fit in.
But when we try to bring in the 65th item, we will need to throw one of them out to make room for the new item. This bring us to the third type of cache misses: Capacity Miss.
+3 = 41 min. (Y:21)

## Slide 9: Where does a Block Get Placed in a Cache?
Example: Block 12 placed in 8 block cache
0 1 2 3 4 5 6 7
Block
no.
Direct mapped:
block 12 can go only into block 4 (12 mod 8)
Set associative:
block 12 can go anywhere in set 0 (12 mod 4)
0 1 2 3 4 5 6 7
Block
no.
Set
0
Set
1
Set
2
Set
3
Fully associative:
block 12 can go anywhere
0 1 2 3 4 5 6 7
Block
no.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
32-Block Address Space:
1 1 1 1 1 1 1 1 1 1 2 2 2 2 2 2 2 2 2 2 3 3
Block
no.

## Slide 10: Which block should be replaced on a miss?
Easy for Direct Mapped: Only one possibility
Set Associative or Fully Associative:
  Random
  LRU (Least Recently Used)
Miss rates for a workload:
2-way 4-way 8-way Size LRU Random LRU Random LRU Random
16 KB 5.2% 5.7% 4.7% 5.3% 4.4% 5.0%
64 KB 1.9% 2.0% 1.5% 1.7% 1.4% 1.5%
256 KB 1.15% 1.17% 1.13% 1.13% 1.12% 1.12%

## Slide 11: Review: What happens on a write?
Write through: The information is written to both the block in the cache and to the block in the lower-level memory
Write back: The information is written only to the block in the cache
  Modified cache block is written to main memory only when it is replaced
  Question is block clean or dirty?
Pros and Cons of each?
  WT:
    PRO: read misses cannot result in writes
    CON: Processor held up on writes unless writes buffered
  WB:
    PRO: repeated writes not sent to DRAM processor not held up on writes
    CON: More complex Read miss may require writeback of dirty data

## Slide 12: Recall: What TLB Organization Makes Sense?
Needs to be really fast
  Critical path of memory access
    In simplest view: before the cache
    Thus, this adds to access time (reducing cache speed)
  Seems to argue for Direct Mapped or Low Associativity
However, needs to have very few conflicts!
  With TLB, the Miss Time extremely high! (PT traversal)
  Cost of Conflict (Miss Time) is high
  Hit Time – dictated by clock cycle
Thrashing: continuous conflicts between accesses
  What if use low order bits of page as index into TLB?
    First page of code, data, stack may map to same entry
    Need 3-way associativity at least?
  What if use high order bits as index?
    TLB mostly unused for small programs
CPU
TLB
Cache
[Physically
indexed]
Memory

## Slide 13: Physically-Indexed vs Virtually-Indexed Caches
Physically-Indexed Caches
  Address handed to cache after translation
  Page Table holds physical addresses
  Benefits:
    Every piece of data has single place in cache
    Cache can stay unchanged on context switch
  Challenges:
    TLB is in critical path of lookup!
  Pretty Common today (e.g., x86 processors)
Virtually-Indexed Caches
  Address handed to cache before translation
  Page Table holds virtual addresses (one option)
  Benefits:
    TLB not in critical path of lookup, so can be faster
  Challenges:
    Same data could be mapped in multiple places of cache
    May need to flush cache on context switch
We will stick with Physically Addressed Caches for now!
CPU
Cache
[Virtually
indexed]
Memory
[Virtually
addressed] Page Table
TLB

offset
virtual
virtual
virtual
physical
CPU
Cache
[Physically
indexed]
Memory
[Physically
addressed] Page Table
TLB

offset
physical
virtual
physical
physical

## Slide 14: Reducing translation time for physically-indexed caches
As described, TLB lookup is in serial with cache lookup
  Consequently, speed of TLB can impact speed of access to cache
Machines with TLBs go one step further: overlap TLB lookup with cache access
  Works because offset available early
  Offset in virtual address exactly covers the “cache index” and “byte select”
  Thus can select the cached byte(s) in parallel to perform address translation
Virtual Address
TLB Lookup
V
Access
Rights
PA
V page no.
offset
10
P page no.
offset
10
Physical Address
Offset
Virtual Page #
index
tag / page #
byte
virtual address:
physical address:

## Slide 15: Overlapping TLB & Cache Access
Here is how this might work with a 4K cache:
What if cache size is increased to 8KB?
  Overlap not complete
  Need to do something else. See CS152/252
Another option: Virtual Caches would make this faster
  Tags in cache are virtual addresses
  Translation only happens on cache misses
TLB
4K Cache
10
2
00
4 bytes
index
1 K
page #
disp
20
assoc
lookup
32
Hit/
Miss
FN
Data
Hit/
Miss
=
FN

## Slide 16: Putting Everything Together: Address Translation
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
PageTablePtr
Page Table
(1st level)
Page Table
(2nd level)
Physical
Memory:
Offset
Physical Address:
Physical
Page #

## Slide 17: Putting Everything Together: TLB
Page Table
(2nd level)
PageTablePtr
Page Table
(1st level)
Offset
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
Physical
Memory:
Physical Address:
…
TLB:
Physical
Page #
Physical
Page #

## Slide 18: Putting Everything Together: Cache
Page Table
(2nd level)
PageTablePtr
Page Table
(1st level)
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
…
TLB:
Offset
Physical
Memory:
Physical Address:
…
tag:
block:
cache:
index
byte
tag
Physical
Page #

## Slide 20: Administrivia
Midterm 2: Coming up on next Thursday 3/18 5-6:30PM (one weeks from today)
  Topics: up and including Lecture 16: Scheduling, Deadlock, Address Translation, Virtual Memory, Caching, TLBs, Demand Paging
  Lecture 16 will be released early
  Will REQUIRE you to have your zoom proctoring setup working again
    You must have screen sharing (entire desktop not just the browser), audio unmuted, and your camera working
    Make sure to get your setup debugged and ready!
Review Session: 3/16 (5-7pm)
  Details TBA

## Slide 22: TLB organization: include protection
How big does TLB actually have to be?
  Usually small: 128-512 entries (larger now)
  Not very big, can support higher associativity
Small TLBs usually organized as fully-associative cache
  Lookup is by Virtual Address
  Returns Physical Address + other info
What happens when fully-associative is too slow?
  Put a small (4-16 entry) direct-mapped cache in front
  Called a “TLB Slice”
Example for MIPS R3000:
0xFA00 0x0003 Y N Y R/W 34 0x0040 0x0010 N Y Y R 0 0x0041 0x0011 N Y Y R 0
Virtual Address Physical Address Dirty Ref Valid Access ASID

## Slide 23: Example: R3000 pipeline includes TLB “stages”
Inst Fetch
Dcd/ Reg
ALU / E.A
Memory
Write Reg
TLB I-Cache RF Operation WB
E.A. TLB D-Cache
MIPS R3000 Pipeline
ASID
V. Page Number
Offset
12
20
6
0xx User segment (caching based on PT/TLB entry)
100 Kernel physical space, cached
101 Kernel physical space, uncached
11x Kernel virtual space
Allows context switching among
64 user processes without TLB flush
Virtual Address Space
TLB
  64 entry, on-chip, fully associative, software TLB fault handler

## Slide 24: Current Intel x86 (Skylake, Cascade Lake)

## Slide 25: Current Example: Memory Hierarchy
Caches (all 64 B line size)
  L1 I-Cache: 32 KiB/core, 8-way set assoc.
  L1 D Cache: 32 KiB/core, 8-way set assoc., 4-5 cycles load-to-use, Write-back policy
  L2 Cache: 1 MiB/core, 16-way set assoc., Inclusive, Write-back policy, 14 cycles latency
  L3 Cache: 1.375 MiB/core, 11-way set assoc., shared across cores, Non-inclusive victim cache, Write-back policy, 50-70 cycles latency
TLB
  L1 ITLB, 128 entries; 8-way set assoc. for 4 KB pages
    8 entries per thread; fully associative, for 2 MiB / 4 MiB page
  L1 DTLB 64 entries; 4-way set associative for 4 KB pages
    32 entries; 4-way set associative, 2 MiB / 4 MiB page translations:
    4 entries; 4-way associative, 1G page translations:
  L2 STLB: 1536 entries; 12-way set assoc. 4 KiB + 2 MiB pages
    16 entries; 4-way set associative, 1 GiB page translations:

## Slide 26: What happens on a Context Switch?
Need to do something, since TLBs map virtual addresses to physical addresses
  Address Space just changed, so TLB entries no longer valid!
Options?
  Invalidate TLB: simple but might be expensive
    What if switching frequently between processes?
  Include ProcessID in TLB
    This is an architectural solution: needs hardware
What if translation tables change?
  For example, to move page from memory to disk or vice versa…
  Must invalidate TLB entry!
    Otherwise, might think that page is still in memory!
  Called “TLB Consistency”
Aside: with Virtually-Indexed cache, need to flush cache!
  Rember, everyone has their own version of the address “0”!

## Slide 27: Recall: Page Fault
The Virtual-to-Physical Translation fails
  PTE marked invalid, Priv. Level Violation, Access violation, or does not exist
  Causes a Fault / Trap
    Not an interrupt because synchronous to instruction execution
  May occur on instruction fetch or data access
  Protection violations typically terminate the instruction
Other Page Faults engage operating system to fix the situation and retry the instruction
  Allocate an additional stack page, or
  Make the page accessible - Copy on Write,
  Bring page in from secondary storage to memory – demand paging
Fundamental inversion of the hardware / software boundary

## Slide 28: Demand Paging
Modern programs require a lot of physical memory
  Memory per system growing faster than 25%-30%/year
But they don’t use all their memory all of the time
  90-10 rule: programs spend 90% of their time in 10% of their code
  Wasteful to require all of user’s code to be in memory
Solution: use main memory as “cache” for disk
On-Chip
Cache
Control
Datapath
Secondary
Storage
(Disk)
Processor
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
Tertiary
Storage
(Tape)
paging
caching

## Slide 29: Page Fault  Demand Paging
virtual address
MMU
PT
instruction
physical address
page#
frame#
offset
page fault
Operating System
exception
Page Fault Handler
load page from disk
update PT entry
Process
scheduler
retry
frame#
offset

## Slide 30: Demand Paging as Caching, …
What “block size”? - 1 page (e.g., 4 KB)
What “organization” i.e., direct-mapped, set-assoc., fully-associative?
  Fully associative since arbitrary virtual  physical mapping
How do we locate a page?
  First check TLB, then page-table traversal
What is page replacement policy? (i.e., LRU, Random…)
  This requires more explanation… (kinda LRU)
What happens on a miss?
  Go to lower level to fill miss (i.e., disk)
What happens on a write? (write-through, write back)
  Definitely write-back – need dirty bit!

## Slide 31: Illusion of Infinite Memory
Page
Table
TLB
Disk is larger than physical memory 
  In-use virtual memory can be bigger than physical memory
  Combined memory of running processes much larger than physical memory
    More programs fit into memory, allowing more concurrency
Principle: Transparent Level of Indirection (page table)
  Supports flexible placement of physical data
    Data could be on disk or somewhere across network
  Variable location of data transparent to user program
    Performance issue, not correctness issue
Physical
Memory
512 MB
Disk
500GB

Virtual
Memory
4 GB

## Slide 32: Review: What is in a PTE?
What is in a Page Table Entry (or PTE)?
  Pointer to next-level page table or to actual page
  Permission bits: valid, read-only, read-write, write-only
Example: Intel x86 architecture PTE:
  2-level page table (10, 10, 12-bit offset)
  Intermediate page tables called “Directories”
  P: Present (same as “valid” bit in other architectures)
  W: Writeable
  U: User accessible
  PWT: Page write transparent: external cache write-through
  PCD: Page cache disabled (page cannot be cached)
  A: Accessed: page has been accessed recently
  D: Dirty (PTE only): page has been modified recently
  PS: Page Size: PS=14MB page (directory only). Bottom 22 bits of virtual address serve as offset
Page Frame Number
(Physical Page Number)
Free
(OS)
0
PS
D
A
PCD
PWT
U
W
P
0
1
2
3
4
5
6
7
8
11-9
31-12

## Slide 33: Demand Paging Mechanisms
Cache
PTE makes demand paging implementable
  Valid  Page in memory, PTE points at physical page
  Not Valid  Page not in memory; use info in PTE to find it on disk when necessary
Suppose user references page with invalid PTE?
  Memory Management Unit (MMU) traps to OS
    Resulting trap is a “Page Fault”
  What does OS do on a Page Fault?:
    Choose an old page to replace
    If old page modified (“D=1”), write contents back to disk
    Change its PTE and any cached TLB to be invalid
    Load new page into memory from disk
    Update page table entry, invalidate TLB for new entry
    Continue thread from original faulting location
  TLB for new page will be loaded when thread continued!
  While pulling pages off disk for one process, OS runs another process from ready queue
    Suspended process sits on wait queue

## Slide 35: Origins of Paging
Disks provide most of the storage
Relatively small memory, for many processes
P
. . .
Many clients on dumb terminals running different programs
Keep memory full of the frequently accesses pages
Keep most of the address space on disk
Actively swap pages to/from

## Slide 36: Very Different Situation Today
Powerful system
Huge memory
Huge disk
Single user

## Slide 37: The View on One Machine
Memory stays about 75% used, 25% for dynamics
A lot of it is shared 1.9 GB

## Slide 38: Many Uses of Virtual Memory and “Demand Paging” …
Extend the stack
  Allocate a page and zero it
Extend the heap (sbrk of old, today mmap)
Process Fork
  Create a copy of the page table
  Entries refer to parent pages – NO-WRITE
  Shared read-only pages remain shared
  Copy page on write
Exec
  Only bring in parts of the binary in active use
  Do this on demand
MMAP to explicitly share region (or to access a file as RAM)

## Slide 39: Classic: Loading an Executable into Memory
.exe
  lives on disk in the file system
  contains contents of code & data segments, relocation entries and symbols
  OS loads it into memory, initializes registers (and initial stack pointer)
  program sets up stack and heap upon initialization: crt0 (C runtime init)
disk (huge)
memory
code
data
info
exe

## Slide 40: Create Virtual Address Space of the Process
Utilized pages in the VAS are backed by a page block on disk
  Called the backing store or swap file
  Typically, in an optimized block store, but can think of it like a file
disk (huge)
memory
code
data
heap
stack
kernel
process VAS
sbrk
kernel code & data
user page
frames
user pagetable

## Slide 41: Create Virtual Address Space of the Process
User Page table maps entire VAS
All the utilized regions are backed on disk
  swapped into and out of memory as needed
For every process
disk (huge, TB)
memory
code
data
heap
stack
kernel
process VAS (GBs)
kernel code & data
user page
frames
user pagetable
code
data
heap
stack

## Slide 42: Create Virtual Address Space of the Process
User Page table maps entire VAS
Resident pages mapped to the frame in memory they occupy
The portion of page table that the HW needs to access must be resident in memory
disk (huge, TB)
memory
code
data
heap
stack
kernel
VAS
[per process]
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
PT

## Slide 43: Provide Backing Store for VAS
User Page table maps entire VAS
Resident pages mapped to the frame in memory they occupy
For all other pages, OS must record where to find them on disk
disk (huge, TB)
memory
code
data
heap
stack
kernel
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
VAS
[per process]

## Slide 44: What Data Structure Maps Non-Resident Pages to Disk?
FindBlock(PID, page#) → disk_block
  Some OSs utilize spare space in PTE for paged blocks
  Like the PT, but purely software
Where to store it?
  In memory – can be compact representation if swap storage is contiguous on disk
  Could use hash table (like Inverted PT)
Usually want backing store for resident pages too
May map code segment directly to on-disk image
  Saves a copy of code to swap file
May share code segment with multiple instances of the program

## Slide 45: Provide Backing Store for VAS
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data

## Slide 46: On Page Fault …
disk (huge, TB)
memory
kernel code
& data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 47: On Page Fault … Find & Start Load
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 48: On page Fault … schedule other P or T
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 49: On Page Fault … Update PTE
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 50: Eventually reschedule faulting thread
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 51: Summary: Steps in Handling a Page Fault

## Slide 53: Some Questions We Need to Answer!
During a page fault, where does the OS get a free frame?
  Keeps a free list
  Unix runs a “reaper” if memory gets too full
    Schedule dirty pages to be written back on disk
    Zero (clean) pages which haven’t been accessed in a while
  As a last resort, evict a dirty page first
How can we organize these mechanisms?
  Work on the replacement policy
How many page frames/process?
  Like thread scheduling, need to “schedule” memory resources:
    Utilization? fairness? priority?
  Allocation of disk paging bandwidth

## Slide 54: Working Set Model
As a program executes it transitions through a sequence of “working sets” consisting of varying sized subsets of the address space
Time
Address

## Slide 55: Cache Behavior under WS model
Amortized by fraction of time the Working Set is active
Transitions from one WS to the next
Capacity, Conflict, Compulsory misses
Applicable to memory caches and pages. Others ?
Hit Rate
Cache Size
new working set fits
0
1

## Slide 56: Another Model of Locality: Zipf
Likelihood of accessing item of rank r is α 1/ra
Although rare to access items below the top few, there are so many that it yields a “heavy tailed” distribution
Substantial value from even a tiny cache
Substantial misses from even a very large cache
Chart: P access(rank) = 1/rank
pop a=1 | 0.19278 | 0.096388 | 0.064259 | 0.048194 | 0.038555 | 0.032129 | 0.027539 | 0.024097 | 0.02142 | 0.019278 | 0.017525 | 0.016065 | 0.014829 | 0.01377 | 0.012852 | 0.012048 | 0.01134 | 0.01071 | 0.010146 | 0.0096388 | 0.0091798 | 0.0087625 | 0.0083815 | 0.0080323 | 0.007711 | 0.0074144 | 0.0071398 | 0.0068848 | 0.0066474 | 0.0064259 | 0.0062186 | 0.0060242 | 0.0058417 | 0.0056699 | 0.0055079 | 0.0053549 | 0.0052102 | 0.005073 | 0.004943 | 0.0048194 | 0.0047018 | 0.0045899 | 0.0044832 | 0.0043813 | 0.0042839 | 0.0041908 | 0.0041016 | 0.0040162 | 0.0039342 | 0.0038555
Hit Rate(cache) | 0.19278 | 0.28916 | 0.35342 | 0.40162 | 0.44017 | 0.4723 | 0.49984 | 0.52394 | 0.54536 | 0.56463 | 0.58216 | 0.59822 | 0.61305 | 0.62682 | 0.63967 | 0.65172 | 0.66306 | 0.67377 | 0.68392 | 0.69356 | 0.70274 | 0.7115 | 0.71988 | 0.72791 | 0.73562 | 0.74304 | 0.75018 | 0.75706 | 0.76371 | 0.77014 | 0.77635 | 0.78238 | 0.78822 | 0.79389 | 0.7994 | 0.80475 | 0.80996 | 0.81504 | 0.81998 | 0.8248 | 0.8295 | 0.83409 | 0.83857 | 0.84296 | 0.84724 | 0.85143 | 0.85553 | 0.85955 | 0.86348 | 0.86734

## Slide 57: Demand Paging Cost Model
Since Demand Paging like caching, can compute average access time! (“Effective Access Time”)
  EAT = Hit Rate x Hit Time + Miss Rate x Miss Time
  EAT = Hit Time + Miss Rate x Miss Penalty
Example:
  Memory access time = 200 nanoseconds
  Average page-fault service time = 8 milliseconds
  Suppose p = Probability of miss, 1-p = Probably of hit
  Then, we can compute EAT as follows:
EAT = 200ns + p x 8 ms
= 200ns + p x 8,000,000ns
If one access out of 1,000 causes a page fault, then EAT = 8.2 μs:
  This is a slowdown by a factor of 40!
What if want slowdown by less than 10%?
  EAT < 200ns x 1.1  p < 2.5 x 10-6
  This is about 1 page fault in 400,000!

## Slide 58: Page Replacement Policies
Why do we care about Replacement Policy?
  Replacement is an issue with any cache
  Particularly important with pages
    The cost of being wrong is high: must go to disk
    Must keep important pages in memory, not toss them out
FIFO (First In, First Out)
  Throw out oldest page. Be fair – let every page live in memory for same amount of time.
  Bad – throws out heavily used pages instead of infrequently used
RANDOM:
  Pick random page for every replacement
  Typical solution for TLB’s. Simple hardware
  Pretty unpredictable – makes it hard to make real-time guarantees
MIN (Minimum):
  Replace page that won’t be used for the longest time
  Great (provably optimal), but can’t really know future…
  But past is a good predictor of the future …

## Slide 59: Summary (1/2)
The Principle of Locality:
  Program likely to access a relatively small portion of the address space at any instant of time.
    Temporal Locality: Locality in Time
    Spatial Locality: Locality in Space
Three (+1) Major Categories of Cache Misses:
  Compulsory Misses: sad facts of life. Example: cold start misses.
  Conflict Misses: increase cache size and/or associativity
  Capacity Misses: increase cache size
  Coherence Misses: Caused by external processors or I/O devices
Cache Organizations:
  Direct Mapped: single block per set
  Set associative: more than one block per set
  Fully associative: all entries equivalent
Notes: Let’s summarize today’s lecture. I know you have heard this many times and many ways but it is still worth repeating.
Memory hierarchy works because of the Principle of Locality which says a program will access a relatively small portion of the address space at any instant of time.
There are two types of locality: temporal locality, or locality in time and spatial locality, or locality in space.
So far, we have covered three major categories of cache misses.
Compulsory misses are cache misses due to cold start. You cannot avoid them but if you are going to run billions of instructions anyway, compulsory misses usually don’t bother you.
Conflict misses are misses caused by multiple memory location being mapped to the same cache location.
The nightmare scenario is the ping pong effect when a block is read into the cache but before we have a chance to use it, it was immediately forced out by another conflict miss.
You can reduce Conflict misses by either increase the cache size or increase the associativity, or both.
Finally, Capacity misses occurs when the cache is not big enough to contains all the cache blocks required by the program. You can reduce this miss rate by making the cache larger.
There are two write policy as far as cache write is concerned. Write through requires a write buffer and a nightmare scenario is when the store occurs so frequent that you saturates your write buffer.
The second write polity is write back. In this case, you only write to the cache and only when the cache block is being replaced do you write the cache block back to memory.
+3 = 77 min. (Y:57)

## Slide 60: Summary
“Translation Lookaside Buffer” (TLB)
  Small number of PTEs and optional process IDs (< 512)
  Often Fully Associative (Since conflict misses expensive)
  On TLB miss, page table must be traversed and if located PTE is invalid, cause Page Fault
  On change in page table, TLB entries must be invalidated
Demand Paging: Treating the DRAM as a cache on disk
  Page table tracks which pages are in memory
  Any attempt to access a page that is not in memory generates a page fault, which causes OS to bring missing page into memory
Replacement policies
  FIFO: Place pages on queue, replace page at end
  MIN: Replace page that will be used farthest in future
  LRU: Replace page used farthest in past