## Slide 1: CS162 Operating Systems and Systems Programming Lecture 18 Storage Devices, Performance, Queuing Theory

## Slide 2: Recall : Simplified IO architecture
Follows a hierarchical structure because of cost: the faster the bus, the more expensive it is

## Slide 3: Recall: How does the processor talk to devices?
Remember, it’s all about abstractions!
Interface
(What the OS sees)
Internals
(What is needed to implement the abstraction)
Hardware interface device presents to OS
Hardware interface device presents to OS
Microcontroller
Memory
Other chips
Device Controller
Status
Command
Data

## Slide 4: Recall: Device Drivers
Device Driver: Device-specific code in the kernel that interacts directly with the device hardware
  Supports a standard, internal interface
  Special device-specific configuration supported with the ioctl() system call
Device Drivers typically divided into two pieces:
  Top half: accessed in call path from system calls
    implements a set of standard, cross-device calls like open(), close(), read(), write(), ioctl(), strategy()
    This is the kernel’s interface to the device driver
    Top half will start I/O to device, may put thread to sleep until finished
  Bottom half: run as interrupt routine
    Gets input or transfers next block of output
    May wake sleeping threads if I/O now complete
Your body is 90% water, the OS is 70% device-drivers

## Slide 5: Recall: Life Cycle of An I/O Request
Device Driver
Top Half
Device Driver
Bottom Half
Device
Hardware
Kernel I/O
Subsystem
User
Program

## Slide 6: Ways of Measuring Performance: Times (s) and Rates (op/s)
Response Time or Latency - time to complete a task
  Measured in units of time (s, ms, us, …, hours, years)
Throughput or Bandwidth – rate at which tasks are performed
  Measured in units of things per unit time (ops/s, GFLOP/s)
Start up or Overhead – time to initiate an operation
Most I/O operations are roughly linear in b bytes
  Latency(b) = Overhead + b/TransferCapacity

## Slide 7: Storage Devices
Magnetic disks
  Storage that rarely becomes corrupted
  Large capacity at low cost
  Block level random access (except for SMR – later!)
  Slow performance for random access
  Better performance for sequential access
Flash memory
  Storage that rarely becomes corrupted
  Capacity at intermediate cost (5-20x disk)
  Block level random access
  Good performance for reads; worse for random writes
  Wear patterns issue

## Slide 8: Hard Disk Drives (HDDs)
Read/Write Head Side View
IBM Personal Computer 1986
30MB Hard Disk for 500 dollars

## Slide 9: The Amazing Magnetic Disk
Store data magnetically on thin metallic film bonded to rotating disk of glass, ceramic, or aluminum

## Slide 10: The Amazing Magnetic Disk
Store data magnetically on thin metallic film bonded to rotating disk of glass, ceramic, or aluminum
Track: concentric circle on surface
Sectors: slice of a track
  Smallest addressable unit
  Are units of transfers
Cylinder all the tracks under the head at a given point
on all surfaces

## Slide 11: The Amazing Magnetic Disk
Sector
Track
Cylinder
Head
Platter
Track lengths vary across disk: outside tracks have more sectors per track, higher bandwidth
Disk is organized into regions of tracks with the same number of sector/tracks
Usually, only outer half of radius is used

## Slide 12: The Amazing Magnetic Disk
Read/write data is a three-stage process:
  Seek time: position the head/arm over the proper track
  Rotational latency: wait for desired sector to rotate under r/w head
  Transfer time: transfer a block of bits (sector) under r/w head
Software
Queue
(Device Driver)
Hardware
Controller
Media Time
(Seek+Rot+Xfer)
Request
Result
Request Time = Queueing Time + Controller Time + Seek + Rotational + Transfer

## Slide 13: Typical Numbers for Magnetic Disk
Parameter | Info/Range
Space/Density | Space: 14TB (Seagate), 8 platters, in 3½ inch form factor! Areal Density: ≥ 1 Terabit/square inch! (PMR, Helium, …)
Average Seek Time | Typically 4-6 milliseconds
Average Rotational Latency | Most laptop/desktop disks rotate at 3600-7200 RPM (16-8 ms/rotation). Server disks up to 15,000 RPM. Average latency is halfway around disk so 4-8 milliseconds
Controller Time | Depends on controller hardware
Transfer Time | Typically 50 to 250 MB/s. Depends on: Transfer size (usually a sector): 512B – 1KB per sector Rotation speed: 3600 RPM to 15000 RPM Recording density: bits per inch on a track Diameter: ranges from 1 in to 5.25 in
Cost | Used to drop by a factor of two every 1.5 years (or faster), now slowing down

## Slide 14: Disk Performance Example
Key to using disk effectively (especially for file systems) is to minimize seek and rotational delays
Assumptions:
  Ignoring queuing and controller times for now
  Avg seek time of 5ms,
  7200RPM  Time for rotation: 60000 (ms/min) / 7200(rev/min) ~= 8ms
  Transfer rate of 50MByte/s, block size of 4Kbyte  4096 bytes/50×106 (bytes/s) = 81.92 × 10-6 sec  0.082 ms for 1 sector

## Slide 15: Disk Performance Example
Read block from random place on disk (random reads):
  Seek (5ms) + Rot. Delay (4ms) + Transfer (0.082ms) = 9.082ms
  Approx 9ms to fetch/put data: 4096 bytes/9.082×10-3 s  451KB/s
Read block from random place in same cylinder:
  Rot. Delay (4ms) + Transfer (0.082ms) = 4.082ms
  Approx 4ms to fetch/put data: 4096 bytes/4.082×10-3 s  1.03MB/s
Read next block on same track (sequential reads):
  Transfer (0.082ms): 4096 bytes/0.082×10-3 s  50MB/sec

## Slide 16: Lots of Intelligence in the Controller
Sectors contain sophisticated error correcting codes
  Disk head magnet has a field wider than track
  Hide corruptions due to neighboring track writes
Sector sparing
  Remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
Track skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential ops

## Slide 17: Hard Drive Prices over Time

## Slide 18: Example of Current HDDs
Seagate Exos X18 (2020)
  18 TB hard disk
    9 platters, 18 heads
    Helium filled: reduce friction and power
  4.16ms average seek time
  4096 byte physical sectors
  7200 RPMs
  Dual 6 Gbps SATA /12Gbps SAS interface
    270MB/s MAX transfer rate
    Cache size: 256MB
  Price: $ 562 (~ $0.03/GB)
IBM Personal Computer/AT (1986)
  30 MB hard disk
  30-40ms seek time
  0.7-1 MB/s (est.)
  Price: $500 ($17K/GB, 340,000x more expensive !!)

## Slide 19: Solid State Drives
1995 – Replace rotating magnetic media with non-volatile memory (battery backed DRAM)
2009 – Use flash memory
  Sector (4 KB page) addressable, but stores 4-64 “pages” per memory block
  Trapped electrons distinguish between 1 and 0
No moving parts (no rotate/seek motors)
  Eliminates seek and rotational delay (0.1-0.2ms access time)
  Very low power and lightweight
  Limited “write cycles”
Rapid advances in capacity and cost ever since!

## Slide 20: The Flash Cell
Encode bit by trapping electrons into a cell
Single-level cell (SLC)
  Single bit is stored within a transistor
  Faster, more lasting (50k to 100k writes before wear out)
Multi-level cell (MLC)
  Two/three bits are encoded into different levels of charge
  Wear out much faster (1k to 10k writes)

## Slide 21: Of banks, blocks, cells
Bank
Block
Block
Page
Page
Page
Page
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Flash chips organized in banks
  Banks can be accessed in parallel
Blocks: 128 KB/256KB
  (64 to 258 pages)
Pages: Few KB
Cells: 1 to 4 bits
Distinction between blocks and pages important in operations!

## Slide 22: Low-level flash operations
How do you read?
  Chip supports reading pages
  10s of microseconds, independently of the previously read page
What about writing? More complicated!
  Must first erase the block
    Erase quite expensive (milliseconds)
  Once block has been erased, can then program a page
    Change 1s to 0s within a page.
    100s of microseconds.
  Blocks can only be erased a limited number of times!

## Slide 23: Low-level flash operations
INVALID
ERASED
VALID

## Slide 24: Low-level flash operations
Assume block of 4 pages. All valid. Want to write Page 0
Step 1: erase full block
Step 2: program page 0

## Slide 25: SSD Architecture
Recall that SSDs uses low-level Flash operations to provide same interface as HDD
  read and write chunk (4KB) at a time
Reads are easy, but for writes, can only overwrite data one block (256KB) at a time!
Why not just erase and rewrite new version of entire 256KB block?
  Erasure is very slow (milliseconds)
  Each block has a finite lifetime, can only be erased and rewritten about 10K times
  Heavily used blocks likely to wear out quickly

## Slide 26: SSD Architecture (Simplified)

## Slide 27: Flash Translation Layer (FTL)
Add a layer of indirection: the flash translation layer
  Translates request for logical blocks (device interface) to low-level Flash blocks and pages
Goal: performance and reliability
Reduce write amplification
  Ratio of the total write traffic in bytes issues by the flash chip by the FTL devided by the total write traffic issued by the OS to the device
Avoid wear out
  A single block should not be erased too often

## Slide 28: FTL – Two Systems Principles
FTL uses indirection and copy-on-write
Maintains mapping tables in DRAM
  Map virtual block numbers (which OS uses) to physical page numbers (which flash mem. controller uses)
  Can now freely relocate data w/o OS knowing
Copy on Write/ Log-structured FTL
  Don’t overwrite a page when OS updates its data
  Instead, write new version in a free page
  Update FTL mapping to point to new location

## Slide 29: FTL – Two Systems Principles
FTL uses indirection and copy-on-write
Maintains mapping tables in DRAM
  Map virtual block numbers (which OS uses) to physical page numbers (which flash mem. controller uses)
  Can now freely relocate data w/o OS knowing
Copy on Write/ Log-structured FTL
  Don’t overwrite a page when OS updates its data
  Instead, write new version in a free page
  Update FTL mapping to point to new location

## Slide 30: FTL Example
Write(a0)
Block 0
Block 1
Mapping Table
a0->0,0
a0
V
E
E
E
Block 0
Block 1
Mapping Table:
E
E
E
E
Initial
State
Write(a1)
Block 0
Block 1
Mapping Table:
a0->0,0/a1->0,1
a0
a1
V
V
E
E
Write(a1)
Block 0
Block 1
Mapping Table:
a0->0,0/a1->1,0
a0
a1
V
V
a1
V
E
Write(a1)
Block 0
Block 1
Mapping Table:
a0->1,1/a1->1,0
a0
a1
V
V
a1
a0
V
V
Garbage Collect
Block 0
Block 1
Mapping Table:
a0->1,1/a1->1,0
E
E
a1
a0
V
V

## Slide 31: Some “Current” (large) 3.5in SSDs
Seagate Exos SSD: 15.36TB (2017)
  Seq reads 860MB/s
  Seq writes 920MB/s
  Price (Amazon): $5495 ($0.36/GB)
Nimbus SSD: 100TB (2019)
  Seq reads/writes: 500MB/s
  Random Read Ops (IOPS): 100K
  Unlimited writes for 5 years!
  Price: ~ $40K? ($0.4/GB)
    However, 50TB drive costs $12500 ($0.25/GB)

## Slide 32: HDD vs. SSD Comparison
HDD | SDD
Require seek + rotation | No seeks
Not parallel (one head) | Parallel
Brittle (moving parts) | No moving parts
Random reads take 10s milliseconds | Random reads take 10s microseconds
Slow (Mechanical) | Wears out
Cheap/large storage | Expensive/smaller storage

## Slide 33: Recall: Overall Performance for I/O Path
Performance of I/O subsystem
  Metrics: Response Time, Throughput
Contributing factors to latency:
    Software paths (can be loosely modeled by a queue)
    Hardware controller
    I/O device service time
Queuing behavior:
  Can lead to big increases of latency as utilization increases
  Solutions?
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 34: Sequential Server Performance
Single sequential “server” that can complete a task in time operates at rate (on average, in steady state, …)
  →
L
L
L
L
…
time
L

## Slide 35: Single Pipelined Server
Single pipelined server of stages for tasks of length (i.e., time per stage) delivers at rate .
  , →
L
…
L
L
L
L
L
L
L
L
logical operation
divided over distinct resources
time

## Slide 36: Multiple Servers
servers handling tasks of length delivers at rate .
  , →
L
…
k

## Slide 37: A Simple Systems Performance Model
Bandwidth (): Rate, Op/s
e.g., flow: gal per min
Latency (): time per op
How long does it take to flow through the system
If and
How much water is “in the system?”

## Slide 38: A Simple Systems Performance Model
Bandwidth (): Rate, Op/s
e.g., flow: gal per min
Latency (): time per op
How long does it take to flow through the system
If and
How many ops are “in the system?”

## Slide 39: A Simple Systems Performance Model
If and
How many ops are “in the system?”
B=1/3
B=2/3
B=1
B=4/3
B=5/3s
B=2

## Slide 40: Little’s Law (B  )
In any stable system
  Average arrival rate = Average departure rate
The number of “things” in a system is equal to the bandwidth times the latency (on average)
  N (jobs) = λ (jobs/s) x L (s)
  Applies to any stable system
Can be applied to an entire system:
  Including the queues, the processing stages, parallelism, whatever
Or to just one processing stage:
  i.e., disk I/O subsystem, queue leading into a CPU or I/O stage, …
arrivals
departures
N
λ
L

## Slide 41: A Simple Systems Performance Model
Request Rate:
Service Rate:
Operation Time:
Queuing delay:
Latency ()
The maximum service rate is a property of the system – the “bottleneck”
Utilization:

## Slide 42: Ideal System Performance
How does (service rate) vary with (request rate)?
Request Rate ( ) - “offered load”
Service Rate () - “delivered load”
asymptotic peak rate

## Slide 43: Two Related Questions
Request Rate:
Operation Time:
Latency ()
The maximum service rate is a property of the system – the “bottleneck”
Utilization:
Service Rate:
Queuing delay:
What determines ?
What about “internal” queues?

## Slide 44: Bottleneck Analysis
…
L
L
L
L
L
L
L
time
Overall System: Series of Stages
Request Rate:
Service Rate:

## Slide 45: Bottleneck Analysis
Each stage has its own queue and maximum service rate
Suppose the green stage is the bottleneck
Overall System: Series of Stages
Request Rate:
Service Rate:

## Slide 46: Bottleneck Analysis
Each stage has its own queue and maximum service rate
Suppose the green stage is the bottleneck
The bottleneck stage dictates the maximum service rate
System Model: Bottleneck Stage
Request Rate:
Service Rate:

## Slide 47: Example: Servicing a Highly Contended Lock
…
…
sec in critical section
All try to grab lock
Time = sec
Rate = ops/sec, regardless of # cores
Queue of waiting threads
Critical section guarded by lock

## Slide 48: Two Related Questions
Request Rate:
Operation Time:
Latency ()
The maximum service rate is a property of the system – the “bottleneck”
Utilization:
Service Rate:
Queuing delay:
is service rate of bottleneck stage
Tank represents queue of bottleneck stage

## Slide 49: Queuing
What happens when request rate () exceeds max service rate ()?
Short bursts can be absorbed by the queue
  If on average it will drain eventually
Prolonged → queue will grow without bound

## Slide 50: A Simple, Deterministic World
Assume requests arrive at regular intervals, take a fixed time to process, with plenty of time between …
Queue
Server
arrivals
departures
: time between arrivals
: service time
: queuing time

## Slide 51: A Simple, Deterministic World
Utilization ()
Delivered Throughput
0
1
1
time
Queue delay
Delivered Throughput
0
1
1
Utilization ()
Empty Queue
Saturation
Unbounded
time
Queue delay

## Slide 52: A Bursty World
Requests arrive in a burst, must queue up until served
Same average arrival time, but almost all of the requests experience large queue delays (even though average utilization is low)
Queue
Server
arrivals
departures
: time between arrivals
  Now, a random variable
: service time
: queuing time
Q depth
Server
Arrivals

## Slide 53: How to model burstiness of arrival?
, the time between arrivals, is now a random variable
  Elegant mathematical framework if we model it as an exponential distribution
  Probability distribution function of an exponential distribution with parameter is
Chart: 
| 1E-3 | 0.01 | 0.02 | 0.04 | 0.08 | 0.16 | 0.32 | 0.64 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 10
 | 0.999 | 0.99005 | 0.9802 | 0.96079 | 0.92312 | 0.85214 | 0.72615 | 0.52729 | 0.36788 | 0.13534 | 0.049787 | 0.018316 | 0.0067379 | 0.0024788 | 0.00091188 | 0.00033546 | 4.54e-05
Lots of short arrival intervals (i.e., high instantaneous rate)
Few long gaps (i.e., low instantaneous rate)
x (λ)
mean arrival interval (1/λ)
“Memoryless”: Likelihood of an event occurring is independent of how long we’ve been waiting

## Slide 54: Steady State Queuing Theory
Queuing Theory applies to long term, steady state behavior
  Arrival rate = Departure rate
Arrivals characterized by some probabilistic distribution
Departures characterized by some probabilistic distribution
Departures
Arrivals
Queuing System
Queue
Server

## Slide 55: Little’s Law Applied to a Queue
When applied to a queue, we get:
Average length of the queue
Average Arrival Rate
Average time “waiting”

## Slide 56: Some Results from Queuing Theory
Assumptions: system in equilibrium, no limit to the queue, time between successive arrivals is random and memoryless
Arrival Rate
Queue
Server
Service Rate
: service rate ()
: utilization ()
: arrival rate
: mean time to service a customer
: squared coefficient of variance ()

## Slide 57: Some Results from Queuing Theory
Memoryless service distribution (—an “M/M/1 queue”:
General service distribution (no restrictions)—an “M/G/1 queue”:
: service rate ()
: utilization ()
: arrival rate
: mean time to service a customer
: squared coefficient of variance ()

## Slide 58: Some Results from Queuing Theory (con’t)
(memoryless service distribution)
(by Little’s Law)
Utilization is , so
(for a single server)

## Slide 59: Ideal System Performance
Request Rate ( ) - “offered load”
Service Rate () - “delivered load”
Latency ()
Time
,
Why does latency blow up as we approach 100% utilization?
  Queue builds up on each burst
  But very rarely (or never) gets a chance to drain

## Slide 60: A Little Queuing Theory: An Example
Example Usage Statistics:
  User requests 10 x 8KB disk I/Os per second
  Requests & service exponentially distributed (C=1.0)
  Avg. service = 20 ms (From controller+seek+rot+trans)
Questions:
  How utilized is the disk?
    Ans: server utilization,  = Tser
  What is the average time spent in the queue?
    Ans: Tq
  What is the number of requests in the queue?
    Ans: Lq
  What is the avg response time for disk request?
    Ans: Tsys = Tq + Tser
Computation:
 (avg # arriving customers/s) = 10/s
Tser (avg time to service customer) = 20 ms (0.02s)
 (server utilization) =  x Tser= 10/s x .02s = 0.2
Tq (avg time/customer in queue) = Tser x u/(1 – u) = 20 x 0.2/(1-0.2) = 20 x 0.25 = 5 ms (0 .005s)
Lq (avg length of queue) =  x Tq=10/s x .005s = 0.05
Tsys (avg time/customer in system) =Tq + Tser= 25 ms

## Slide 61: Conclusion
Two types of storage devices:
  HDDs, which are organized as a set of platters split into tracks, which are being spinned by a motor. HDDs have suffer from rotational delay and high seek latency
  SDDs are built on top of flash technology. Flash offers three operations: read, write, program
  SDDs do not suffer from seek/rotation delay but suffer from wear out.
Performance
  Bottleneck & queueing delay
  Model arrival/departure rate as probability distributions