## Slide 1: CS162 Operating Systems and Systems Programming Lecture 24 Networking and TCP/IP (Con’t), RPC, Distributed File Systems
April 21st, 2022
Prof. Anthony Joseph and John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Distributed Consensus Making
Consensus problem
  All nodes propose a value
  Some nodes might crash and stop responding
  Eventually, all remaining nodes decide on the same value from set of proposed values
Distributed Decision Making
  Choose between “true” and “false”
  Or Choose between “commit” and “abort”
Equally important (but often forgotten!): make it durable!
  How do we make sure that decisions cannot be forgotten?
    This is the “D” of “ACID” in a regular database
  In a global-scale system?
    What about erasure coding or massive replication?
    Like BlockChain applications!

## Slide 3: Recall: Two-Phase Commit Protocol
Persistent stable log on each machine: keep track of whether commit has happened
  If a machine crashes, when it wakes up it first checks its log to recover state of world at time of crash
Prepare Phase:
  The global coordinator requests that all participants will promise to commit or rollback the transaction
  Participants record promise in log, then acknowledge
  If anyone votes to abort, coordinator writes "Abort" in its log and tells everyone to abort; each records "Abort" in log
Commit Phase:
  After all participants respond that they are prepared, then the coordinator writes "Commit" to its log
  Then asks all nodes to commit; they respond with ACK
  After receive ACKs, coordinator writes "Got Commit" to log
Log used to guarantee that all machines either commit or don’t

## Slide 4: Distributed Decision Making Discussion (1/2)
Why is distributed decision making desirable?
  Fault Tolerance!
  A group of machines can come to a decision even if one or more of them fail during the process
    Simple failure mode called “failstop” (different modes later)
  After decision made, result recorded in multiple places
Why is 2PC not subject to the General’s paradox?
  Because 2PC is about all nodes eventually coming to the same decision – not necessarily at the same time!
  Allowing us to reboot and continue allows time for collecting and collating decisions

## Slide 5: Distributed Decision Making Discussion (2/2)
Undesirable feature of Two-Phase Commit: Blocking
  One machine can be stalled until another site recovers:
    Site B writes "prepared to commit" record to its log, sends a "yes" vote to the coordinator (site A) and crashes
    Site A crashes
    Site B wakes up, check its log, and realizes that it has voted "yes" on the update. It sends a message to site A asking what happened. At this point, B cannot decide to abort, because update may have committed
    B is blocked until A comes back
  A blocked site holds resources (locks on updated items, pages pinned in memory, etc) until learns fate of update

## Slide 6: Alternatives to 2PC
Three-Phase Commit: One more phase, allows nodes to fail or block and still make progress.
PAXOS: An alternative used by Google and others that does not have 2PC blocking problem
  Develop by Leslie Lamport (Turing Award Winner)
  No fixed leader, can choose new leader on fly, deal with failure
  Some think this is extremely complex!
RAFT: PAXOS alternative from John Osterhout (Stanford)
  Simpler to describe complete protocol
What happens if one or more of the nodes is malicious?
  Malicious: attempting to compromise the decision making
  Use a more hardened decision making process: Byzantine Agreement and Block Chains

## Slide 7: Byzantine General’s Problem
Byazantine General’s Problem (n players):
  One General and n-1 Lieutenants
  Some number of these (f) can be insane or malicious
The commanding general must send an order to his n-1 lieutenants such that the following Integrity Constraints apply:
  IC1: All loyal lieutenants obey the same order
  IC2: If the commanding general is loyal, then all loyal lieutenants obey the order he sends
General
Attack!
Attack!
Attack!
Retreat!
Attack!
Retreat!
Attack!
Attack!
Attack!
Lieutenant
Lieutenant
Lieutenant
Malicious!

## Slide 8: Byzantine General’s Problem (con’t)
Impossibility Results:
  Cannot solve Byzantine General’s Problem with n=3 because one malicious player can mess up things
  With f faults, need n > 3f to solve problem
Various algorithms exist to solve problem
  Original algorithm has #messages exponential in n
  Newer algorithms have message complexity O(n2)
    One from MIT, for instance (Castro and Liskov, 1999)
Use of BFT (Byzantine Fault Tolerance) algorithm
  Allow multiple machines to make a coordinated decision even if some subset of them (< n/3 ) are malicious
General
Lieutenant
Lieutenant
Attack!
Attack!
Retreat!
General
Lieutenant
Lieutenant
Attack!
Retreat!
Retreat!
Request
Distributed
Decision

## Slide 9: Is a BlockChain a Distributed Decision Making Algorithm?
BlockChain: a chain of blocks connected by hashes to root block
  The Hash Pointers are unforgeable (assumption)
  The Chain has no branches except perhaps for heads
  Blocks are considered “authentic” part of chain when they have authenticity info in them
How is the head chosen?
  Some consensus algorithm
  In many BlockChain algorithms (e.g. BitCoin, Ethereum), the head is chosen by solving hard problem
    This is the job of “miners” who try to find “nonce” info that makes hash over block have specified number of zero bits in it
    The result is a “Proof of Work” (POW)
    Selected blocks above (green) have POW in them and can be included in chains
  Longest chain wins
Hash Ptr
Root
Block
The “Block Chain”
Tentative Head #2
Tentative Head #1

## Slide 10: Is a Blockchain a Distributed Decision Making Algorithm? (Con’t)
Decision means: Proposal is locked into BlockChain
  Could be Commit/Abort decision
  Could be Choice of Value, State Transition, ….
NAK: Didn’t make it into the block chain (must retry!)
Anyone in world can verify the result of decision making!
Hash Ptr
Root
Block
Miner:
Tries to solve POW problem
Hash Ptr
Root
Block
Miner:
Tries to solve POW problem
Hash Ptr
Root
Block
Miner:
Tries to solve POW problem
Hash Ptr
Root
Block
Observer:
Tracks state of BlockChain
Hash Ptr
Root
Block
Observer:
Tracks state of BlockChain
Hash Ptr
Root
Block
Observer:
Tracks state of BlockChain
Hash Ptr
Root
Block
Observer:
Tracks state of BlockChain
Hash Ptr
Root
Block
Observer:
Tracks state of BlockChain
Hash Ptr
Root
Block
Observer:
Tracks state of BlockChain
Proposal
Proposal
Epidemic
Replication
Hash Ptr
Root
Block
Observer:
Tracks state of BlockChain
Hash Ptr
Root
Block
Observer:
Tracks state of BlockChain
Hash Ptr
Root
Block
Observer:
Tracks state of BlockChain

## Slide 11: Network Protocols
Networking protocols: many levels
  Physical level: mechanical and electrical network (e.g., how are 0 and 1 represented)
  Link level: packet formats/error control (for instance, the CSMA/CD protocol)
  Network level: network routing, addressing
  Transport Level: reliable message delivery
Protocols on today’s Internet:
Ethernet
WiFi
LTE
IP
UDP
TCP
RPC
NFS
WWW
e-mail
ssh
Physical/Link
Network
Transport

## Slide 12: Broadcast Networks
Broadcast Network: Shared Communication Medium
  Shared Medium can be a set of wires
    Inside a computer, this is called a bus
    All devices simultaneously connected to devices
  Originally, Ethernet was a broadcast network
    All computers on local subnet connected to one another
  More examples (wireless: medium is air): cellular phones (GSM, CDMA, and LTE), WiFi
Memory
Processor
I/O
Device
I/O
Device
I/O
Device
Internet

## Slide 13: Broadcast Networks Details
Media Access Control (MAC) Address:
  48-bit physical address for hardware interface
  Every device (in the world!?) has a unique address
Delivery: When you broadcast a packet, how does a receiver know who it is for? (packet goes to everyone!)
  Put header on front of packet: [ Destination MAC Addr | Packet ]
  Everyone gets packet, discards if not the target
  In Ethernet, this check is done in hardware
    No OS interrupt if not for particular destination
Header
(Dest:2)
Body
(Data)
Message
ID:1
(ignore)
ID:2
(receive)
ID:4
(ignore)
ID:3
(sender)

## Slide 14: Carrier Sense, Multiple Access/Collision Detection
Ethernet (early 80’s): first practical local area network
  It is the most common LAN for UNIX, PC, and Mac
  Use wire instead of radio, but still broadcast medium
Key advance was in arbitration called CSMA/CD: Carrier sense, multiple access/collision detection
  Carrier Sense: don’t send unless idle
    Don’t mess up communications already in process
  Collision Detect: sender checks if packet trampled.
    If so, abort, wait, and retry.
  Backoff Scheme: Choose wait time before trying again
How long to wait after trying to send and failing?
  What if everyone waits the same length of time? Then, they all collide again at some time!
  Must find way to break up shared behavior with nothing more than shared communication channel
Adaptive randomized waiting strategy:
  Adaptive and Random: First time, pick random wait time with some initial mean. If collide again, pick random value from bigger mean wait time. Etc.
  Randomness is important to decouple colliding senders
  Scheme figures out how many people are trying to send!

## Slide 15: MAC Address: Unique Physical Address of Interface
Can easily find MAC addr. on your machine/device:
  E.g., ifconfig (Linux, Mac OS X), ipconfig (Windows)
Transport
Network
Session
Present.
Application
Datalink
Physical
Wi-Fi MAC address
Wired/Ethernet MAC address

## Slide 16: Point-to-point networks
Why have a shared bus at all? Why not simplify and only have point-to-point links + routers/switches?
  Originally wasn’t cost-effective, now hardware is cheap!
Point-to-point network: a network in which every physical wire is connected to only two computers
Switch: a bridge that transforms a shared-bus (broadcast) configuration into a point-to-point network
  Adaptively figures out which ports have which MAC addresses
Router: a device that acts as a junction between physical networks to transfer data packets among them
  Routes between switching domains using (for instance) IP addresses
Router
Internet
Switch

## Slide 17: The Internet Protocol (IP)
Internet Protocol: Internet’s network layer
Service it provides: “Best-Effort” Packet Delivery
  Tries it’s “best” to deliver packet to its destination
  Packets may be lost
  Packets may be corrupted
  Packets may be delivered out of order
IP Is a Datagram service!
  Routes across many physical switching domains (subnets)
source
destination
IP network
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 18: IPv4 Address Space
IP Address: a 32-bit integer used as destination of IP packet
  Often written as four dot-separated integers, with each integer from 0—255 (thus representing 8x4=32 bits)
  Example CS file server is: 169.229.60.83  0xA9E53C53
Internet Host: a computer connected to the Internet
  Host has one or more IP addresses used for routing
    Some of these may be private and unavailable for routing
  Not every computer has a unique IP address
    Groups of machines may share a single IP address
    In this case, machines have private addresses behind a “Network Address Translation” (NAT) gateway
Subnet: network connecting hosts with related IP addresses
  A subnet is identified by 32-bit value, with the bits which differ set to zero, followed by a slash and a mask
    Example: 128.32.131.0/24 designates a subnet in which all the addresses look like 128.32.131.XX
    Same subnet: 128.32.131.0/255.255.255.0
  Mask: The number of matching prefix bits
    Expressed as a single value (e.g., 24) or a set of ones in a 32-bit value (e.g., 255.255.255.0)
  Often routing within subnet is by MAC address (smart switches)

## Slide 19: Address Ranges in IPv4
IP address space divided into prefix-delimited ranges:
  Class A: NN.0.0.0/8
    NN is 1–126 (126 of these networks)
    16,777,214 IP addresses per network
    10.xx.yy.zz is private
    127.xx.yy.zz is loopback
  Class B: NN.MM.0.0/16
    NN is 128–191, MM is 0-255 (16,384 of these networks)
    65,534 IP addresses per network
    172.[16-31].xx.yy are private
  Class C: NN.MM.LL.0/24
    NN is 192–223, MM and LL 0-255 (2,097,151 of these networks)
    254 IP addresses per networks
    192.168.xx.yy are private
Address ranges are often owned by organizations
  Can be further divided into subnets

## Slide 20: IPv4 Packet Format
IP Packet Format:
IP Datagram: an unreliable, unordered, packet sent from source to destination
  Function of network – deliver datagrams!
16-bit identification
ToS
4
13-bit frag off
Total length(16-bits)
protocol
TTL
16-bit header checksum
32-bit source IP address
32-bit destination IP address
IHL
flags
options (if any)
Data
0
15
16
31
IP Ver4
IP Header
Length
Size of datagram
(header+data)
Flags &
Fragmentation
to split large
messages
Time to
Live (hops)
Type of
transport
protocol
IP header
20 bytes

## Slide 21: Wide Area Network
Wide Area Network (WAN): network that covers a broad area (e.g., city, state, country, entire world)
  E.g., Internet is a WAN
WAN connects multiple physical (datalink) layer networks (LANs)
Datalink layer networks are connected by routers
  Different LANs can use different communication technology (e.g., wireless, cellular, optics, wired)
Host A
(IP A)
Host B
(IP B)
R2
R3
R4
R1

## Slide 22: Routers
Forward each packet received on an incoming link to an outgoing link based on packet’s destination IP address (towards its destination)
Store & forward: packets are buffered before being forwarded
Forwarding table: mapping between IP address and the output link
incoming links
outgoing links
Router
Memory

## Slide 23: Packet Forwarding
Upon receiving a packet, a router
  read the IP destination address of the packet
  consults its forwarding table  output port
  forwards packet to corresponding output port
Default route (for subnets without explicit entries)
  Forward to more authoritative router
Host A
(IP A)
Host B
(IP B)
R2
R3
R4
R1
IP B

## Slide 24: IP Addresses vs. MAC Addresses
Why not use MAC addresses for routing?
  Doesn’t scale
Analogy
  MAC address  SSN
  IP address  (unreadable) home address
MAC address: uniquely associated with device for the entire lifetime of the device
IP address: changes as the device location changes
  Your notebook IP address at school is different from home
10 7th Street NW
Washington, DC 21115
1051 Euclid Ave
Berkeley, CA 94722

## Slide 25: IP Addresses vs. MAC Addresses
Why does packet forwarding using IP addr. scale?
Because IP addresses can be aggregated
  E.g., all IP addresses at UC Berkeley start with 0xA9E5, i.e., any address of form 0xA9E5**** belongs to Berkeley
  Thus, a router in NY needs to keep a single entry for all hosts at Berkeley
  If we were using MAC addresses the NY router would need to maintain an entry for every Berkeley host!!
Analogy:
  Give this letter to person with SSN: 123-45-6789 vs.
  Give this letter to “John Smith, 123 First Street, LA, US”

## Slide 26: Setting up Routing Tables
How do you set up routing tables?
  Internet has no centralized state!
    No single machine knows entire topology
    Topology constantly changing (faults, reconfiguration, etc.)
  Need dynamic algorithm that acquires routing tables
    Ideally, have one entry per subnet or portion of address
    Could have “default” routes that send packets for unknown subnets to a different router that has more information
Possible algorithm for acquiring routing table
  Routing table has “cost” for each entry
    Includes number of hops to destination, congestion, etc.
    Entries for unknown subnets have infinite cost
  Neighbors periodically exchange routing tables
    If neighbor knows cheaper route to a subnet, replace your entry with neighbors entry (+1 for hop to neighbor)
In reality:
  Internet has networks of many different scales
  Different algorithms run at different scales

## Slide 27: Administrivia
Midterm 3: Thursday 4/28: 7-9PM
  All course material
  Review session Monday 4/25 1-3PM

## Slide 28: Naming in the Internet
How to map human-readable names to IP addresses?
  E.g. www.berkeley.edu  128.32.139.48
  E.g. www.google.com  different addresses depending on location, and load
Why is this necessary?
  IP addresses are hard to remember
  IP addresses change:
    Say, Server 1 crashes gets replaced by Server 2
    Or – google.com handled by different servers
Mechanism: Domain Naming System (DNS)
Name
Address


## Slide 29: Domain Name System
DNS is a hierarchical mechanism for naming
  Name divided in domains, right to left: www.eecs.berkeley.edu
Each domain owned by a particular organization
  Top level handled by ICANN (Internet Corporation for Assigned Numbers and Names)
  Subsequent levels owned by organizations
Resolution: series of queries to successive servers
Caching: queries take time, so results cached for period of time
Top-level
com
edu
Mit.edu
169.229.131.81
128.32.61.103
128.32.139.48
berkeley.edu
www
calmail
eecs
berkeley
MIT
eecs.berkeley.edu
www

## Slide 30: How Important is Correct Resolution?
If attacker manages to give incorrect mapping:
  Can get someone to route to server, thinking that they are routing to a different server
    Get them to log into “bank” – give up username and password
Is DNS Secure?
  Definitely a weak link
    What if “response” returned from different server than original query?
    Get person to use incorrect IP address!
  Attempt to avoid substitution attacks:
    Query includes random number which must be returned
In July 2008, hole in DNS security located!
  Dan Kaminsky (security researcher) discovered an attack that broke DNS globally
    One person in an ISP convinced to load particular web page, then all users of that ISP end up pointing at wrong address
  High profile, highly advertised need for patching DNS
    Big press release, lots of mystery
    Security researchers told no speculation until patches applied

## Slide 31: Network Layering
Layering: building complex services from simpler ones
  Each layer provides services needed by higher layers by utilizing services provided by lower layers
The physical/link layer is pretty limited
  Packets are of limited size (called the “Maximum Transfer Unit or MTU: often 200-1500 bytes in size)
  Routing is limited to within a physical link (wire) or perhaps through a switch
Our goal in the following is to show how to construct a secure, ordered, message service routed to anywhere:
Physical Reality: Packets | Abstraction: Messages
Limited Size (MTU) | Arbitrary Size
Unordered (sometimes) | Ordered
Unreliable | Reliable
Machine-to-machine | Process-to-process
Only on local area net | Routed anywhere
Asynchronous | Synchronous
Insecure | Secure

## Slide 32: Recall: IPv4 Packet Format
IP Packet Format:
IP Datagram: an unreliable, unordered, packet sent from source to destination
  Function of network – deliver datagrams!
16-bit identification
ToS
4
13-bit frag off
Total length(16-bits)
protocol
TTL
16-bit header checksum
32-bit source IP address
32-bit destination IP address
IHL
flags
options (if any)
Data
0
15
16
31
IP Ver4
IP Header
Length
Size of datagram
(header+data)
Flags &
Fragmentation
to split large
messages
Time to
Live (hops)
Type of
transport
protocol
IP header
20 bytes

## Slide 33: Building a messaging service on IP
Process to process communication
  Basic routing gets packets from machinemachine
  What we really want is routing from processprocess
    Add “ports”, which are 16-bit identifiers
    A communication channel (connection) defined by 5 items: [source addr, source port, dest addr, dest port, protocol]
For example: The Unreliable Datagram Protocol (UDP)
  Layered on top of basic IP (IP Protocol 17)
    Datagram: an unreliable, unordered, packet sent from source user  dest user (Call it UDP/IP)
  Important aspect: low overhead!
    Often used for high-bandwidth video streams
    Many uses of UDP considered “anti-social” – none of the “well-behaved” aspects of (say) TCP/IP
UDP Data
16-bit UDP length
16-bit UDP checksum
16-bit source port
16-bit destination port
IP Header
(20 bytes)

## Slide 34: Internet Architecture: Five Layers
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
sockets
sockets

## Slide 35: Internet Architecture: Five Layers
Communication goes down to physical network
Then from network peer to peer
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
sockets
sockets

## Slide 36: Layering Analogy: Packets in Envelopes
101010100110101110
Physical Layer
Physical Layer
101010100110101110
Datalink Layer
Trans.
Hdr.
Net.
Hdr.
Frame
Hdr.
Datalink Layer
Trans.
Hdr.
Net.
Hdr.
Frame
Hdr.
Data
Data
Network Layer
Trans.
Hdr.
Net.
Hdr.
Network Layer
Trans.
Hdr.
Net.
Hdr.
Data
Data
Transport Layer
Trans.
Hdr.
Transport Layer
Trans.
Hdr.
Data
Data
Data
Application Layer
Application Layer
Data
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 37: Internet Transport Protocols
Datagram service (UDP): IP Protocol 17
  No-frills extension of “best-effort” IP
  Multiplexing/Demultiplexing among processes
Reliable, in-order delivery (TCP): IP Protocol6
  Connection set-up & tear-down
  Discarding corrupted packets (segments)
  Retransmission of lost packets (segments)
  Flow control
  Congestion control
Other examples:
  DCCP (33), Datagram Congestion Control Protocol
  RDP (26), Reliable Data Protocol
  SCTP (132), Stream Control Transmission Protocol
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 38: Recall: Sockets in concept
Client
Server
read response
Close Client Socket
Create Client Socket
Connect it to server (host:port)
Create Server Socket
Bind it to an Address
(host:port)
Listen for Connection
Close Connection Socket
Close Server Socket
write request
write response
Accept syscall()
Connection Socket
Connection Socket
read request

## Slide 39: Reliable Message Delivery: the Problem
All physical networks can garble and/or drop packets
  Physical media: packet not transmitted/received
    If transmit close to maximum rate, get more throughput – even if some packets get lost
    If transmit at lowest voltage such that error correction just starts correcting errors, get best power/bit
  Congestion: no place to put incoming packet
    Point-to-point network: insufficient queue at switch/router
    Broadcast link: two host try to use same link
    In any network: insufficient buffer space at destination
    Rate mismatch: what if sender send faster than receiver can process?
Reliable Message Delivery on top of Unreliable Packets
  Need some way to make sure that packets actually make it to receiver
    Every packet received at least once
    Every packet received at most once
  Can combine with ordering: every packet received by process at destination exactly once and in order

## Slide 40: Transmission Control Protocol (TCP)
Transmission Control Protocol (TCP)
  TCP (IP Protocol 6) layered on top of IP
  Reliable byte stream between two processes on different machines over Internet (read, write, flush)
TCP Details
  Fragments byte stream into packets, hands packets to IP
    IP may also fragment by itself
  Uses window-based acknowledgement protocol (to minimize state at sender and receiver)
    “Window” reflects storage at receiver – sender shouldn’t overrun receiver’s buffer space
    Also, window should reflect speed/capacity of network – sender shouldn’t overload network
  Automatically retransmits lost packets
  Adjusts rate of transmission to avoid congestion
    A “good citizen”
Router
Router
Stream in:
Stream out:
..zyxwvuts
gfedcba

## Slide 41: Problem: Dropped Packets
All physical networks can garble or drop packets
  Physical hardware problems (bad wire, bad signal)
Therefore, IP can garble or drop packets
  It doesn't repair this itself (end-to-end principle!)
Building reliable message delivery
  Confirm that packets aren't garbled
  Confirm that packets arrive exactly once

## Slide 42: Using Acknowledgements
How to ensure transmission of packets?
  Detect garbling at receiver via checksum, discard if bad
  Receiver acknowledges (by sending “ACK”) when packet received properly at destination
  Timeout at sender: if no ACK, retransmit
Some questions:
  If the sender doesn’t get an ACK, does that mean the receiver didn’t get the original message?
    No
  What if ACK gets dropped? Or if message gets delayed?
    Sender doesn’t get ACK, retransmits, Receiver gets message twice, ACK each
B
A
Packet
ACK
B
A
Packet
ACK
Packet
Timeout
Notes: - So how can we ensure delivery of packets over an unreliable network?

## Slide 43: Stop-and-Wait (No Packet Loss)
Send; wait for ACK; repeat
Round Trip Time (): time it takes a packet to travel from sender to receiver and back
  One-way latency (): one way delay from sender and receiver
For symmetric latency,
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT
d

## Slide 44: Stop-and-Wait (No Packet Loss)
How fast can you send data?
Little’s Law applied to the network:
For Stop-and-Wait, packet
So bandwidth is 1 packet per RTT
  Depends only on latency, not network capacity (!)
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT
d

## Slide 45: Stop-and-Wait (No Packet Loss)
So bandwidth is 1 packet per RTT
  Depends only on latency, not network capacity (!)
Suppose RTT = 100 ms and 1 packet is 1500 bytes
Throughput = = 120 Kbps
Very inefficient if we have a 100 Mbps link!
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT
d

## Slide 46: Stop-and-Wait with Packet Loss
Loss recovery relies on timeouts
How to choose a good timeout?
  Too short – lots of duplication
  Too long – packet loss is really disruptive!
How to deal with duplication?
  Retransmission certainly opens up the possibility for
ACK 1
Time
Sender
Receiver
1
RTT
timeout
1

## Slide 47: How to Deal with Message Duplication?
Solution: put sequence number in message to identify re-transmitted packets
  Receiver checks for duplicate number’s; Discard if detected
Requirements:
  Sender keeps copy of unACK’d messages
    Easy: only need to buffer messages
  Receiver tracks possible duplicate messages
    Hard: when ok to forget about received message?
Alternating-bit protocol:
  Send one message at a time; don’t send next message until ACK received
  Sender keeps last message; receiver tracks sequence number of last message received
Pros: simple, small overhead
Con: doesn’t work if network can delay or duplicate messages arbitrarily
Pkt #0
ACK #0
Pkt #1
ACK #1
Pkt #0
ACK #0
Sender
Receiver

## Slide 48: Advantages of Moving Away From Stop-and-Wait
Larger space of acknowledgements
  Pipelining: don’t wait for ACK before sending next packet
ACKs serve dual purpose:
  Reliability: Confirming packet received
  Ordering: Packets can be reordered at destination
How much data is in flight now?
  Bytes in-flight: Wsend = RTT × B
  Here B is in “bytes/second”
  Wsend  Sender’s “Window Size”
  Packets in flight = (Wsend / packet size)
How long does the sender have to keep the packets around?
How long does the receiver have to keep the packets’ data?
What if sender is sending packets faster than the receiver can process the data?
Time
Sender
Receiver
RTT
d

## Slide 49: Recall: Communication Between Processes
Data written by A is held in memory until B reads it
Queue has a fixed capacity
  Writing to the queue blocks if the queue if full
  Reading from the queue blocks if the queue is empty
POSIX provides this abstraction in the form of pipes
write(wfd, wbuf, wlen);
n = read(rfd,rbuf, rmax);
Process A
Process B
In-Memory Queue

## Slide 50: Buffering in a TCP Connection
Host 1
A single TCP connection needs four in-memory queues:
  Send buffer: add data on write syscall, remove data when ACK received
  Receive buffer: add data when packets received, remove data on read syscall
Process A
Send Queue
Receive Queue
Host 2
Process B
Receive Queue
Send Queue
Separate pair of queues per TCP connection
Data (Packets)
Data (Packets)

## Slide 51: Window Size: Space in Receive Queue
Host 1
A host’s window size for a TCP connection is how much remaining space it has in its receive queue
A host advertises its window size in every TCP packet it sends!
Sender never sends more than receiver’s advertised window size
Process A
Send Queue
Receive Queue
Host 2
Process B
Receive Queue
Send Queue
Separate pair of queues per TCP connection
Data (Packets)
Data (Packets)

## Slide 52: Sliding Window Protocol
TCP sender knows receiver’s window size, and aims never to exceed it
But packets that it previously send may arrive, filling the window size!
Rule: TCP sender ensures that:
Number of Sent but UnACKed Bytes < Receiver’s Advertised Window Size
Can send new packets as long as sent-but-unacked packets haven’t already filled the advertised window size

## Slide 53: Sliding Window (No Packet Loss)
Example:Window size () = 3 packets
Window size to fill link is given by:
Bpkt  Packets/sec
Little’s Law once again!
For TCP, window is in bytes, not packets
Time
Sender
Receiver
1
{1}
2
{1, 2}
3
{1, 2, 3}
4
{2, 3, 4}
5
{3, 4, 5}
Unacked packets that sender sent
Out-of-seq packets
in receiver’s window
{}
6
{4, 5, 6}
.
.
.
.
.
.
{}
{}

## Slide 54: TCP Windows and Sequence Numbers: PER BYTE!
Sender has three regions:
  Sequence regions
    sent and ACK’d
    sent and not ACK’d
    not yet sent
  Window (colored region) adjusted by sender
Receiver has three regions:
  Sequence regions
    received and ACK’d (given to application)
    received and buffered
    not yet received (or discarded because out of order)
Sequence Numbers
Sent
not ACK’d
Sent
ACK’d
Not yet
sent
Sender
Not yet
received
Received
Given to app
Received
Buffered
Receiver

## Slide 55: Window-Based Acknowledgements (TCP)
Seq:190
Size:40
Seq:230
A:190/210
Seq:260
A:190/210
Seq:300
A:190/210
Seq:190
A:340/60
Seq:340
A:380/20
Seq:380
A:400/0
A:100/300
Seq:100
A:140/260
Seq:140
A:190/210
100
Seq:100
Size:40
140
Seq:140
Size:50
190
Seq:230
Size:30
230
260
Seq:260
Size:40
300
Seq:300
Size:40
340
Seq:340
Size:40
380
Seq:380
Size:20
400
Retransmit!

## Slide 56: Summary
TCP: Reliable byte stream between two processes on different machines over Internet (read, write, flush)
  Uses window-based acknowledgement protocol
  Congestion-avoidance dynamically adapts sender window to account for congestion in network